## Slide 1: Research on Testing & FP7 BASTION
CEBE-P6
Artur Jutman

## Slide 2: Presentation Outline
No Trouble Found
Embedded Instrumentation
Fault Management against Ageing
Test System for LHC at CERN
FP7 BASTION
A. Jutman CEBE Workshop & IAB, Tallinn, Sept 16, 2013

## Slide 3: Motivation: No Trouble Found – NTF
NTF symptoms
  System passes all tests in the production
  System fails at the customer
  Troubleshooting cannot repeat the failing condition
70% of all product returns characterized as NTF (US, 2008)
an average family (in US) spends annually 65$ on NTF investigations

## Slide 4: Testability Problem: good old days
PCBA
IC
IC
Simple ICs described by functional/truth tables
Sufficient number of test points

## Slide 5: Testability Problem: today
PCBA
BLACK HOLE 2
BLACK HOLE 1
BLACK HOLE 3
Defects might be hiding inside (behind the horizon)
Defects might be spread among the chips (mismatch)
Dynamic defects on the board not covered with functional test
No Trouble Found?

## Slide 6: NTF Cause – Dynamic Faults?
Working Hypothesis
  Conclusion: quality of the existing tests is low
  Main hypothesis: good test methodology for dynamic faults is missing
Test Method | Target Faults | Test Access | Diagnostics | Coverage
Structural | Static only | Scan test, JTAG, intrusive | Good | Good but static only
Functional | Dynamic | Functional code + external measurements | No (pass/fail only) | Unknown
Dream | Dynamic | Non-intrusive | Good | Good (static + dynamic)

## Slide 7: Existing Test Coverage Metrics
MPS | PPVS | PCOLA/SOQ
Material | Value | Correct
 |  | Live
Placement | Presence | Presence
 |  | Alignment
 | Polarity | Orientation
Solder | Solder | Short
 |  | Open
 |  | Quality
Good quality?
Defect free?
Within parametric tolerances?
How to test?
Might be expensive to guarantee and measure
Live
Quality
Coverage of dynamic faults is missing!

## Slide 8: embedded instrumentation
Some Results

## Slide 9: Embedded Instrumentation for Test Access
FPGA
JTAG
NOR
FLASH
I2C
I/O I/O
NAND
FLASH
SPI
FLASH
μP
SRAM
We assume the system has a JTAG port, and a programmable device

## Slide 10: Embedded Instrumentation on FPGA
A new class of instrumentation has been proposed
  Embedded virtual instrumentation (EU+US pat. applications)
  Allows full automation of design, integration, test
Developed instrument examples
  BERT, at-speed test, frequency measurement, etc.
  High-speed in-system programming (flash ICs)
Instruments
External
Embedded
Traditional Virtual Synthetic
Traditional Virtual Synthetic
10

## Slide 11: JTAG-controlled FPGA Instruments

## Slide 12: Microprocessor as an Embedded Tester
Represent the system as a set of tightly interrelated models
Components described using Ec-lipse Modeling Framework (EMF)
Use the models to
  Generate testware
  Create a test access path
  Run test and debug routines
Use HLDDs at all levels as a traversable uniform model
Lego-Style System Modeling

## Slide 13
System
Under
Test
PCBA BOARD
H
E
A
D
E
R
UUT2
UUT1
UUT3
FPGA
Embedded Synthetic Instruments
Instrument
Card
FPGA
Programmable IO
Adaptive Test Bus Controller
General purpose IO instrument card from National Instruments
FPGA on the customer board becomes an embbedded tester
Programmable FPGA on the card becomes an adaptive test bus controller
JTAG standard bus can be used to communicate between the two couterparts
The test object – Unit Under Test
Part of general purpose IO configured as a Test Bus
Typical general purpose functional tester
Customer’s board under test
External PC with control software

## Slide 14: Achievements and future plans
FPGA instrumentation
  Patent applications + PhD by Igor Aleksejev
  Future: intelligent instrumentation
Microprocessors
  PhD by Anton Tšertov
  Future: test OS + real-time test application
Diagnostic Instrumentation for Functional Test
  Status: initial phase, LabVIEW expertise needed
  PhD student needed

## Slide 15: Fault Management against Ageing

## Slide 16: A Fault Tolerant System
Reso-
urce 1
OS + Scheduler
Activity Map
Interrupts
Reso-
urce 2
Reso-
urce N
BIST/BISD, DFT, Fault tolerance machanisms
…
System
Bus

## Slide 17: FM: Going Beyond the Correction
Fault Management (FM) provides co-operation between Fault Tolerance and Resource Management
Failure Resilience = Fault Tolerance + Fault Management + Resource Management
Both online and partly offline (core-wise) procedures combined
Fault detection and recovery/correction is NOT enough
Fault
Manage-
ment
Fault
Tolerance
Fault Detection
Data Recovery/ Rollback
Fault Diagnosis/ Classification
Core/Module Isolation
Statistics Collection
Resource Health Map
(for Resource Management)

## Slide 18: Fault Management Infrastructure
Reso-
urce 1
Fault Manager
OS + Scheduler
Activity Map
System Health Map
Instrument Manager (IM)
DATA
Interrupts
TAP
P1687
MUX
Board Header
JTAG
Minimal
top-level architecture
F
C
X
Reso-
urce 2
Reso-
urce N
Instrument
sub-chains
SIB
…
Resource Manager (RM)
System
Bus
Status register:
failure, corrected, inactive
F
C
X
SIB - Select Instrument Bit

## Slide 19: Logarithmic Scaling
Chart: # of fault monitors (instruments)
| 25 | 50 | 100 | 200 | 500 | 1000
Tworst | 90 | 118 | 158 | 206 | 266 | 326

## Slide 20: Achievements and future plans
Status
  IEEE Design and Test journal paper
  PhD thesis under preparation
  Future: experimental FPGA/ASIC, optimization for target application profiles

## Slide 21: Test System for LHC at CERN
BER Test equipment for the communication channel of CMS

## Slide 22: Communication Channel Under Test
Compact Muon Solenoid
(CMS)
Source: http://cms.web.cern.ch/news/how-cms-detects-particles
ROS
On-detector electronics (CMS)
TSC
Copper twisted pairs
Optical Fiber
Signal translation boards
CMS  ROS: 240 Mbps
CMS  TSC: 480 Mbps
ROS – Read Out Server
TSC – Trigger Sector Collector
Data acquisition system
Copper twisted pairs

## Slide 23: Developed BER Test Equipment
Transmitter and test generator
Receiver and BER counter
Channel under test
NB! Real channel:
Copper twisted pairs: 40m
Optical Fiber: 60m
BER Test algorithms – developed by CEBE engineers
Hardware design and implementation – Testonica Lab + ELIKO
Software and final integration – Testonica Lab
BER – Bit Error Rate

## Slide 24: FP7 BASTION
Board and SoC Test Instrumentation for Ageing and No Failure Found

## Slide 25: Focus Targets of BASTION
The 2012 ITRS lists ageing (NBTI, PBTI, HCI, etc.) in semiconductor devices as one of the few most difficult challenges of process integration that affects reliability.
NFF is being increasingly reported by industry and according to Accenture Report, in 2008 in US, around 70% of all product returns were characterized as NFF. Cost-wise (including returns processing, scrap and liquidation), NFF amounted up to 50% of total 13.8 billion USD (10.5 billion EUR) returns and repairs cost in US, which approximates to 25 USD (19 EUR) per year per capita.

## Slide 26: BASTION:Research Targets and Outcomes
Application Domain
Basic Technology
Key Focus: Ageing
Research targets from Call 11:
decreased reliability;
ageing effects;
heterogeneous SOC integration
Key Focus: No Failure Found
Research targets from Call 11:
modeling for new materials,
processes and devices;
system modeling and simulation
WP1: Fault characterization and test coverage metrics
WP3: Hierarchical in-field ageing test and monitoring
WP4: Instrument-Assisted Testing
for NFF
WP2: Embedded instrumentation networks
Mainly chip-level, in-field test, and monitoring
Mainly board-level, manufacturing test
Graceful degra-dation of SoCs
Reduction of
NFF impact

## Slide 27: BASTION Consortium Composition
Tool Vendors
Universities
Hamm-Lippstadt
Lund
Tallinn
Torino
Twente
End Users
ASTER Technologies
Infineon
Testonica Lab
Project results exploitation value chain:
partners, technologies, tools

## Slide 28: Thank you!