## Slide 1
Tallinn, Estonia
Sergei Kostin, Ph.D.
Department of Computer Systems

## Slide 2: Sergei Kostin (CV)
Education: Tallinn University of Technology
2007–2012 Ph.D. study, Information and Communication Technology,
Ph.D. topic “Self-Diagnosis in Digital Systems”
2006–2007 Master Degree in Computer-and System Engineering, “Fault Diagnosis in the BIST Environment”
2003–2006 Bachelor Degree in Computer-and System Engineering
Career:
2015 – … Research scientist, TTU
2012 – 2015 R&D Engineer, Testonica Lab
2005 – 2011 Development Engineer, TTU
Research topics:
embedded testing and diagnosis of digital circuits
reliability and ageing effects in nanoscale designs

## Slide 3: Tallinn University of Technology 2017

## Slide 4: Faculties and Departments
Notes: Among them

## Slide 5: TTU campus
Library
Economics
Power Engineering
Main buildings
Student hostels
Notes: Other buildings are situated a little bit apart in radius half up to one km.

## Slide 6: Information technology building
Computer Systems

## Slide 7: Research Motivation & Challenges
Lifetime reliability has become one of the key design factors to guarantee CMOS integrated circuit robustness in nanoscale technology
Challenges of technology scaling beyond 65nm: the non-determinism of the devices’ electrical parameters due to time-dependent deviations:
  Hot Carrier Injection (HCI)
  Time-Dependent Dielectric Breakdown(TDDB)
  Electromigration
  Stress voiding
  Interconnect dielectric instability and breakdown
  Negative Bias Temperature Instability (NBTI)

## Slide 8: NBTI Phenomenon
pMOS transistor is under negatively biased condition
complex temperature-dependent physical/chemical process
  causes a degradation of the oxide
  results in a drift of the threshold voltage (∆Vth)
up to 5-15% transistor performance degradation per year
Reaction-diffusion model
GND
VDD
VDD
−VDD
A CMOS invertor gate
pMOS
  Negative Bias Temperature Instability (NBTI)

## Slide 9: Reaction-diffusion model
The illustration of NBTI stress and recovery phases
In case of sufficient recovery phases, the aging process may be slowed down considerably compared to the static NBTI effect.

## Slide 10: NBTI effect modeling
W. Wang, et. al, “The Impact of NBTI Effect on Combinational Circuit:Modeling, Simulation, and Analysis”, 2010
Yu Cao, et. al "Cross-Layer Modeling and Simulation of Circuit Reliability“, 2014
  model dependency of pMOS transistor threshold voltage VTHp shift on input signal probability Pz
PTM 65nm technology
T = 105 ºC
Vth = 1.1V
10 years of aging
These voltage shift values serve as input values for modeling the NBTI-induced gate delays in SPICE simulations.

## Slide 11: SPICE simulation of basic gates
Inverter
n-NAND
n-NOR
Transistor level
Chart: (a) Inverter
| 0 | 9.1250000000000202E-3 | 1.8250000000000034E-2 | 2.7375000000000087E-2 | 3.6500000000000053E-2 | 4.5624999999999999E-2 | 5.475000000000016E-2 | 6.3875000000000001E-2 | 7.3000000000000106E-2 | 8.2125000000000267E-2 | 9.1250000000000067E-2 | 0.10037500000000002 | 0.10950000000000017 | 0.1186250000000003
Delta_t, % | 0 | 0.032258 | 0.048387 | 0.080645 | 0.1129 | 0.12903 | 0.16129 | 0.19355 | 0.22581 | 0.25806 | 0.29032 | 0.32258 | 0.33871 | 0.37097
Chart: (b) 2-input NAND
| 0 | 9.1249999999999994E-3 | 1.8249999999999999E-2 | 2.7375E-2 | 3.6499999999999998E-2 | 4.5624999999999999E-2 | 5.475E-2 | 6.3875000000000001E-2 | 7.2999999999999995E-2 | 8.2125000000000004E-2 | 9.1249999999999998E-2 | 0.10037500000000001 | 0.1095 | 0.11862499999999999
Delta_t, % | 0 | 0.02439 | 0.04878 | 0.060976 | 0.085366 | 0.10976 | 0.13415 | 0.15854 | 0.19512 | 0.23171 | 0.2561 | 0.29268 | 0.31707 | 0.35366
Chart: (c) 2-input NOR
| 0 | 9.1250000000000046E-3 | 1.8249999999999999E-2 | 2.7375000000000045E-2 | 3.6500000000000005E-2 | 4.5624999999999999E-2 | 5.4750000000000076E-2 | 6.3875000000000001E-2 | 7.3000000000000009E-2 | 8.2125000000000045E-2 | 9.1250000000000026E-2 | 0.10037500000000002 | 0.1095000000000001 | 0.11862499999999999
Delta_t1, % | 0 | 0.034188 | 0.059829 | 0.094017 | 0.12821 | 0.16239 | 0.19658 | 0.23077 | 0.26496 | 0.30769 | 0.34188 | 0.38462 | 0.42735 | 0.47863
Dependence of gate output delay on ∆VTHp

## Slide 12: NBTI-induced gate delay degradation modelling
  Δtgate= λ·∆VTHp(xi)+μ·∆VTHp(xi)2
list of λ and μ values is extracted and used to precisely model NBTI-induced path delay degradations
Chart: Inverter (Nominal T=27°C)
| 0 | 9.1250000000000029E-3 | 1.8250000000000002E-2 | 2.7375000000000017E-2 | 3.6500000000000005E-2 | 4.5625000000000006E-2 | 5.4750000000000028E-2 | 6.3875000000000001E-2 | 7.3000000000000009E-2 | 8.2125000000000045E-2 | 9.1250000000000026E-2 | 0.10037500000000002 | 0.10950000000000004 | 0.11862500000000006 | 0.12775 | 0.136875 | 0.14600000000000007 | 0.15512500000000001 | 0.16425000000000001 | 0.173375 | 0.18250000000000008 | 0.19162499999999993 | 0.20075000000000001 | 0.20987500000000001 | 0.21900000000000008 | 0.22812499999999997 | 0.23725000000000004 | 0.24637500000000001 | 0.2555 | 0.264625 | 0.27375000000000005
SPICE 0% | 8.6736e-16 | 0.016667 | 0.033333 | 0.05 | 0.066667 | 0.083333 | 0.11667 | 0.13333 | 0.15 | 0.18333 | 0.2 | 0.23333 | 0.26667 | 0.28333 | 0.31667 | 0.33333 | 0.35 | 0.38333 | 0.4 | 0.43333 | 0.45 | 0.48333 | 0.51667 | 0.53333 | 0.58333 | 0.63333 | 0.68333 | 0.71667 | 0.76667 | 0.81667 | 0.86667
As the result of simulations of individual gates in SPICE a mathematically convenient function (black dash) is matched to each curve characterized with SPICE (blue)

## Slide 13: De-synchronization due to NBTI
occurs when the sum of all gate delays along a given path is larger than the time slack
Time slack
Propagation along path P0 at the start of the circuit lifetime
Propagation along path P0 in 10 years
?
Task: Identify NBTI-induced delay critical paths
NBTI induced delay in 10 years

## Slide 14: NBTI-critical paths identification flow
Obtain technology and environment dependent curve for voltage threshold shift as a function of gate input signal probability ∆VTHp(Pz)
Obtain technology and environment dependent curves for degradation of gate delays as a function of voltage threshold shift (ΔVTHp) for each gate type in the netlist (INV, 2NAND, 2NOR)
  implies one-time SPICE electrical simulations of the individual gates
Simulate the circuit with the stimuli to observe signal probabilities Pz at gate inputs and assign the estimated NBTI-induced gate delays
  Use a suitable technique to identify and calculate NBTI-induced critical path delays
Step 1: ∆VTHp(Pz)
Step 2: (ΔVTHp)
Notes: Obtain technology and environment dependent curve for voltage threshold shift as a function of gate input signal probability ∆VTHp(Pz)
Obtain technology and environment dependent curves for degradation of gate delays as a function of voltage threshold shift Δ_𝑔𝑎𝑡𝑒^𝑁𝐵𝑇𝐼(ΔVTHp) for each gate type in the netlist (INV, 2NAND, 2NOR)
  implies one-time SPICE electrical simulations of the individual gates
Simulate the circuit with the stimuli to observe signal probabilities Pz at gate inputs and assign the estimated NBTI-induced gate delays
  Use a suitable technique to identify and calculate NBTI-induced critical path delays

## Slide 15: Static NBTI-critical path delay calculation
d(Gk) – nominal gate output delay
 (Gk,i) – delay increase by NBTI
t(Gk,i)) =  (Gk,i) + d(Gk)
D(Gk) = max {D(Gi)+ t(Gk,i))Gi  IN(Gk)}
Algorithm 1.
NBTI-aware static timing analysis
FOR all gates Gk, k = 1, 2, …, NG:
t’(Gk,i)=
D(Gk) = max {D(Gi)+ t’(Gk,i)Gi  IN(Gk)}
END FOR
 (Gk,1)
 (Gk,2)
d(Gk)
Gk
No | Gk | G1 | G2 | G3 | G4 | G5 | G6 | G7 | G8 | G9 | G10 | G11
1 | D | 6 | 10 | 15 | 18 | 22 | 28 | 29 | 41 | 34 | 51 | 49
Primary Inputs
Primary Outputs
8
9
6
6
10
6
9
5
5
4
8
3
G1
G2
G3
G4
G5
G6
G7
G9
G10
G11
G8
2
1
2
1
2
3
2
3
3
2
2
1
1
2
3
2
2
1
1
2
1
2

## Slide 16: True critical path terminology
The path is critical when the signal propagation time along it through the circuit is longest compared to the one of any other path
The critical path must be true (functional)
  must exist an input vector pair allowing a transition to actually propagate along the path
length of the path means the time needed for propagating a transition through the path

## Slide 17: A rule set for path length calculation
Tracing the sensitized paths and iterative calculation of path lengths gate by gate:
An input to a gate is said to have controlling value (cv) if it determines the value of the gate output regardless of the values on the other inputs, otherwise, non-controlling value (ncv)
Transition notations: 01 = D1 and 10 = D0
a) single sensitized path through gate
b) several paths with cv, first (fastest) transition taken for calculation
c) several paths with ncv, last (slowest) transition taken
a)
&
xj
xj,v=cv
1
1
…
ncv
D
xk,v
xk
D
b)
&
D0
…
D0
xv = cv
1
1
…
ncv
xk,v
xk
D
c)
&
D1
…
D1
xv = ncv
1
1
…
ncv
xk,v
xk
D

## Slide 18: Rejuvenation stimuli impact
An example of rejuvenation stimuli generation

## Slide 19: Rejuvenation stimuli generation
Zamiacad – scalable hardware design and analysis framework
  parser and elaboration engine that supports VHDL designs
  design simulation, static analysis and other applications for debug
µGP – general-purpose evolutionary toolkit
  generates candidate solutions for rejuvenation stimuli
An general flow of the evolutionary system

## Slide 20: Tasks
Perform experiments with Plasma processor, exercising:
Different real programs (workloads)
  Simple C programs  Assembler  Extract Stimuli
Different architectures: ALU, MULT, Shifter, …
Analyze paths between FFs
Analyze:
footprint of ageing on real functional workloads
Aging-aware program refactoring feasibility

## Slide 21
Thank you!
Sergei Kostin
skostin@ati.ttu.ee